## Slide 1: Lecture 1: Introduction to GIS

## Slide 2
What does GIS stand for?
Geographic
(Geography)
Information
System
Notes: Geography – refers to the Earth surface and near surface.
Spatial refers to any space including geographic
Geospatial is synonymous with geographic.

## Slide 3: What is a Geographic Information System?
Geographic Information System (GIS) – A computer-based system for the collection, storage, organization, maintenance, and analysis of spatially-referenced data, and the output of spatially-referenced information.
  Data – Any collection of related facts; the basic elements of information.
  Information - Data that have been processed to be useful; provides answers to "who", "what", "where", and "when" questions
Information can only come from accurate data (GIGO).
Notes: T

## Slide 4: What are the components of a GIS?
We understand GIS to be computer facilitated system
But it is NOT only software and
hardware
Also includes:
Data – both spatial and aspatial
Trained personnel
Supporting Institution
Protocols for use

## Slide 5
GIS Software Tools
GIS started at universities as research tools – Harvard,
Yale, Minnesota, Clark University
GIS software have evolved to robust (sort of) tools
capable of a wide variety of tasks
Primary flavors
ESRI (ArcGIS) Intergraph QGIS Bentley Map
Microimages Autocad MapInfo
ERDAS Idrisi Manifold Smallworld
GRASS GeoMedia AUTOCAD MAP 3D Maptitude

## Slide 6: The Map

## Slide 7: The Database

## Slide 8: Other Features Graphs
Malarial Deaths per 10,000 People

## Slide 9: Other Features Tables
https://desktop.arcgis.com/en/arcmap/10.3/manage-data/tables/GUID-5A309AD2-B84E-4ECF-A475-7E4B492660EC-web.png

## Slide 10: Other Features Reports
http://desktop.arcgis.com/en/arcmap/10.3/guide-books/extensions/business-analyst/GUID-389C0E81-9313-4C5C-94B0-51D7650E3B53-web.png

## Slide 11: The Power of GIS
The interaction between the database and the map, along with the ability to create graphs, tables and reports.

## Slide 12
GIS allows us to abstract information from the physical world and display it in layers or themes. It allows us to:
Input and edit both spatial and attribute data.
Display data on a screen or print a map.
Analyze the data for making decisions and searching for patterns.
Create models and ask “what if”.
How does a GIS answer spatial questions?

## Slide 13: What types of questions can be answered by a GIS?
Where are particular features found?
What geographic patterns exist?
Where have changes occurred over a specified time period?
Where do certain conditions apply?
What will be the implications if an organization takes a certain action?

## Slide 14: What types of data are used in a GIS?
Coordinate data
Connection information
Descriptive information
Temporal information
Images
Documents
URL’s

## Slide 15: Coordinate Data for a GIS
Spatial data – you can attach coordinate information.
2D maps (X,Y)

## Slide 16: 3D –Maps (X,Y,Z)

## Slide 17: How is spatial data represented in a GIS?
Vectors
Points, Lines & Areas/Polygons
Raster
Grids/Tesselations

## Slide 18: Applications of GIS
Urban Planning, Management & Policy
  Zoning, subdivision planning
  Land acquisition
  Economic development
  Code enforcement
  Housing renovation programs
  Emergency response
  Crime analysis
  Tax assessment
Environmental Sciences
  Monitoring environmental risk
  Modeling storm water runoff
  Management of watersheds, floodplains,
  wetlands, forests, aquifers
  Environmental Impact Analysis
  Hazardous or toxic facility siting
  Groundwater modeling and contamination
  tracking
Political Science
  Redistricting
  Analysis of election results
  Predictive modeling
Civil Engineering/Utility
  Locating underground facilities
  Designing alignment for freeways, transit
  Coordination of infrastructure maintenance
Business
  Demographic Analysis
  Market Penetration/ Share Analysis
  Site Selection
Education Administration
  Attendance Area Maintenance
  Enrollment Projections
  School Bus Routing
Real Estate
  Neighborhood land prices
  Traffic Impact Analysis
  Determination of Highest and Best Use
Health Care
  Epidemiology
  Needs Analysis
  Service Inventory

## Slide 19: GIS Before Computers
Cholera Map of Dr. John Snow (UK 1850s)